Morgan State University
Quantum Laboratory Sequence

Quantum Lab #4: Two-Photon Interference

Reference: Textbook Section

Motivation

[For Eric]

Background

In 1987, Hong, Ou and Mandel (HOM) proposed and demonstrated a quantum interference effect of two photons that has no classical physics counterpart: When two indistinguishable photons combine at a non-polarizing beam splitter at exactly the same time, they always leave together along just one output port of the beam splitter, as shown in Fig. 1.

However, if the two photons arrive at slightly different times at the beam splitter, and are thus distinguishable, each photon will either reflect or transmit in the splitter, independent of the other. Half of the time these two distinguishable photons will (independently) exit along the same port, and half of the time these photons will (independently) exit out separate ports, as shown in Fig. 2. Only in the indistinguishable case will both photons always exit together out one port as a pair.

To better understand how two single photons will behave after entering a beam splitter, some quantum operator theory is helpful. Consider the four ports of a beam splitter as shown in Fig. 2. Let the quantum state be represented as a "ket" containing the number of photons. For example, port 1 with zero photons is represented as \lline 0 \rangle rSub { size 9{1} } . Let the quantum annihilation operator hat a represent the loss of a photon. For example, assume port 1 has one incoming photon, represented as \lline 1 \rangle rSub { size 9{1} } . The removal of this photon is done by operating on this state by hat a , namely {hat a} rSub { size 9{1} } \lline 1 \rangle rSub { size 9{1} } = \lline 0 \rangle rSub { size 9{1} } . Note that the subscripts should match to keep track of the operator on specific ports. To create a photon, we use the photon creation operator {hat a} ^ {nitalic †} , which is the adjoint of {hat a} . For example, to create another photon into port 1, the equation is {hat a} rSub { size 9{1} } rSup {nitalic †} \lline 1 \rangle rSub { size 9{1} } = \lline 2 \rangle rSub { size 9{1} } , which shows that now port 1 has 2 photons entering it.

An amazing fact is that photons can be created out of the vacuum, and in fact this quantum vacuum is a necessary aspect of quantum mechanics, including the explanation for spontaneous emission. The equation to create a photon from the vacuum entering port 1, for example, is {hat a} rSub { size 9{1} } ^{nitalic †} \lline 0 \rangle rSub { size 9{1} } = \lline 1 \rangle rSub { size 9{1} } .

Now, let's investigate how photons entering a beam splitter will behave. To start, assume only vacuum at all ports, i.e. \lline 0 \rangle rSub { size 9{0} } , \lline 0 \rangle rSub { size 9{1} } , \lline 0 \rangle rSub { size 9{2} } , and \lline 0 \rangle rSub { size 9{3} } . Create single photons entering ports 0 and 1:
{hat a} rSub { size 9{0} } rSup {nitalic †} {hat a} rSub { size 9{1} } rSup {nitalic †} \lline 0 \rangle rSub { size 9{0} } \lline 0 \rangle rSub { size 9{1} } = \lline 1 \rangle rSub { size 9{0} } \lline 1 \rangle rSub { size 9{1} }	(1)
As you can see, creation operator {hat a} rSub { size 9{0} } rSup {nitalic †} operates on the vacuum state \lline 0 \rangle rSub { size 9{0} } associated with port 1, and the creation operator {hat a} rSub { size 9{1} } rSup {nitalic †} operates on the vacuum state \lline 0 \rangle rSub { size 9{1} } associated with port 1, resulting in single photons at entry ports 0 and 1.

Referring again to Fig. 2, the creation operator for the output port 2 depends on the photon entering the beam splitter from ports 0 and 1, namely
{hat a} rSub { size 9{2} } rSup {nitalic †} =1 over sqrt{2} ({hat a} rSub { size 9{0} } rSup {nitalic †} -i{hat a} rSub { size 9{1} } rSup {nitalic †})	(2)
and similarly for output port 3:
{hat a} rSub { size 9{3} } rSup {nitalic †} =1 over sqrt{2} ({hat a} rSub { size 9{1} } rSup {nitalic †} -i{hat a} rSub { size 9{0} } rSup {nitalic †})	(3)

Now we can use Eqs. (2) and (3) to solve for {hat a} rSub { size 9{0} } rSup {nitalic †} and {hat a} rSub { size 9{1} } rSup {nitalic †} in terms of {hat a} rSub { size 9{2} } rSup {nitalic †} and {hat a} rSub { size 9{3} } rSup {nitalic †} :
{hat a} rSub { size 9{0} } rSup {nitalic †} =1 over sqrt{2} ({hat a} rSub { size 9{2} } rSup {nitalic †} +i{hat a} rSub { size 9{3} } rSup {nitalic †})	(4a)
{hat a} rSub { size 9{1} } rSup {nitalic †} =1 over sqrt{2} (i{hat a} rSub { size 9{2} } rSup {nitalic †} +{hat a} rSub { size 9{3} } rSup {nitalic †})	(4b)

The relation connecting the ports of the beam splitter can be written as
\lline 0 \rangle rSub { size 9{0} } \lline 0 \rangle rSub { size 9{1} } rightarrow \lline 0 \rangle rSub { size 9{2} } \lline 0 \rangle rSub { size 9{3} }	(5)
Now we can multiply both sides of Eq. (5) by {hat a} rSub { size 9{0} } rSup {nitalic †} {hat a} rSub { size 9{1} } rSup {nitalic †} , and using Eqs. (4):
{hat a} rSub { size 9{0} } rSup {nitalic †}{hat a} rSub { size 9{1} } rSup {nitalic †} \lline 0 \rangle rSub { size 9{0} } \lline 0 \rangle rSub { size 9{1} } rightarrow {hat a} rSub { size 9{0} } rSup {nitalic †}{hat a} rSub { size 9{1} } rSup {nitalic †} \lline 0 \rangle rSub { size 9{2} } \lline 0 \rangle rSub { size 9{3} }= 1 over 2 ({hat a} rSub { size 9{2} } rSup {nitalic †} +i{hat a} rSub { size 9{3} } rSup {nitalic †})(i{hat a} rSub { size 9{2} } rSup {nitalic †} +{hat a} rSub { size 9{3} } rSup {nitalic †}) \lline 0 \rangle rSub { size 9{2} } \lline 0 \rangle rSub { size 9{3} }= i over 2 ( {hat a} rSub { size 9{2} } rSup {nitalic †}{hat a} rSub { size 9{2} } rSup {nitalic †}+{hat a} rSub { size 9{3} } rSup {nitalic †}{hat a} rSub { size 9{3} } rSup {nitalic †})\lline 0 \rangle rSub { size 9{2} } \lline 0 \rangle rSub { size 9{3} }= i over sqrt{ 2 } ( \lline 2 \rangle rSub { size 9{2} } \lline 0 \rangle rSub { size 9{3} }+\lline 0 \rangle rSub { size 9{2} } \lline 2 \rangle rSub { size 9{3} })	(6)

The resulting wave function representing the output of the beam splitter is thus
\lline %psi \rangle = i over sqrt{ 2 } ( \lline 2 \rangle rSub { size 9{2} } \lline 0 \rangle rSub { size 9{3} }+\lline 0 \rangle rSub { size 9{2} } \lline 2 \rangle rSub { size 9{3} })	(7)
Therefore, we see that indistinguishable photons entering a beam splitter will exit together in pairs, with 50% probability exiting port 2 and equally 50% probability exiting port 3.

Figure 3. Illustration of a beam splitter with four ports labeled 1, 2, 3 and 4. Ports 0 and 1 are input ports and ports 2 and 3 are output ports.

Experimental

Each of the quED outputs is connected to one of the inputs of the quED-HOM. We remove the wave plate from the pump beam of the quED, so that we generate indistinguishable non-entangled photon pairs. Now, we can introduce a temporal delay between the two photons by moving one of the fibre collimators in the quED-HOM. This makes the two photons distiguishable (you can say, one photon arrives at the beam splitter “earlier than the other”). We use this to demonstrate the so-called Hong-Ou-Mandel dip in coincidence counts, by tuning the delay between the two photons:

Figure 5. The setup of the two-photon HOM experiment with all necessary connections.

Discussion