## Slide 1
Emergent quantum technology and applications
David Farley
Quantal Technology

## Slide 2
Quantum Truisms
Quantum technologies can potentially be better than classical
Quantum Computing & Software longest time horizon
Quantum Sensing & Encryption here now
Quantum states are fragile
Expertise and suppliers are few

## Slide 3
Quantum Computing – Entangled “Qubits”
Quantum Algorithms - using a quantum computer
Quantum Sensing – ultrasensitive measurements
Quantum Encryption – Unbreakable (in theory)
Qubit = “Quantum Bit” = atom with two states, or photon with two modes
Entangled qubits allow for massively parallel computing
Fundamental Problem: Environment quickly destroys entanglement
Secondary Problem: Expertise and supplies
Only a handful of quantum algorithms proven to enhance computing
Requires programmers who understand quantum
In the future, could enhance pharmaceutical development, etc.
Quantum states are fragile
Quantum sensing leverages quantum sensitivity to environmental perturbations
Opposite situation for quantum computing, where need to isolate from the environment
Quantum Key Distribution (QKD) – relies on non-cloning of quantum wave functions
Shares random numbers between parties
Random numbers for One-Time Pad (OTP) encryption protocol (unbreakable)

## Slide 5
Basic Quantum Theory (“spooky physics”)
Put a “state” into a “ket”: |vertical polarization> =
Now make a “superposition” of pure states:
This wave function is in both the horizontal and vertical states, until measured
Now consider two “entangled” particles (photons):
There is no way to factor out vertical or horizontal states
Quantum computers seek to leverage the entanglement of many particles

## Slide 6
“Qubit” versus “Bit”
A classical computer uses “bits”, which are either a “zero” (0 Volts) or a “one” (5 Volts)
In quantum, we have the “qubit”, which is both a “zero” and a “one”
We can entangle two (or more) qubits:
This is the idea of a quantum computer
Until we measure it
Quantum Advantage Example: Li-3
To simulate the electron wave function for Lithium (N=3 electrons) using a computational grid divided into 3m regions requires a classical computer able to store 23mN amplitudes. To achieve a precision of 10% requires m=3, so 227 bytes needed (500 petabytes!). A quantum computer needs just 27 entangled qubits.

## Slide 7
Quantum Computing
Different Approaches:
Superconducting qubits (pics)
Trapped Ions
Quantum dots
Photons
Others
IBM
Google

## Slide 8
“FPGA control”

## Slide 9
Quantum Algorithms
Quantum computers are useless without quantum algorithms (software):
Currently requires expert knowledge in quantum mechanics and applications
Only a handful of algorithms have been developed that would make a QC better than a classical computer
  Shor’s Algorithm (breaks public-key encryption)
  Grover’s Algorithm (sort a large database faster)

## Slide 10
QUANTUM
SENSORS
Navigation
Gravimetry
Non Destructive Evaluation
Surface Science
Medical Imaging
Timing
Trace Chemical
Detection

## Slide 11
Quantum “Antenna” or Aperture
Atom-bound electrons in a vapor cell monitor RF amplitude subject to laser controls. Shape is not relevant.
Different Physics and Different Limits = Large Opportunity
Established circa 2010
Receive only without inherent “gain”
Photonic processing
ARL
DARPA Quantum Apertures Program
DARPA Envisioned Program End State

## Slide 12
Atom Interferometry (“Quantum Gravity Sensor”)

## Slide 13
Gravimetric signatures are always present as mass cannot be shielded
Gravimetric methods based on atom interferometry may offer a solution for rapid, sensitive detection of buried structures
Detect Underground Structures
Cavity
500m (100m)
Altitude
100m (20m) Diameter
4m
Muquans Instrument
Quantum Gravimetry

## Slide 14
Generation of a MEMSL source using a Beam Splitter Network
Calculated required optical pulse energy vs. desired imaging resolution
Quantum Imaging using Massively Entangled Multimode Squeezed Light (MEMSL)

## Slide 15
Target
Image of target
in other spectral region
Entangled photon source
Quantum “Ghost” imaging

## Slide 16
Secure because can detect Eavesdropper ”Eve”, who disrupts the quantum state
China’s Micius satellite sets distance record for quantum entanglement in space
Part of ambitious Chinese program: Quantum Experiments at Space Scale (QUESS; Chinese: 量子科学实验卫星)
Quantum Key Distribution (QKD) – “Quantum Encryption”

## Slide 17
Unlike current data encryptions standards, which are software-based (e.g. RSA, AES, SHA), QKD relies on hardware:
Lasers (single photon or traditional laser)
Detectors (single photon or homodyne)
Fiber optics
High-speed modulators
ID Quantique Clavis QKD System (Swiss)
Trend is to put all components on a photonic chip
QKD requires hardware unlike Public Keys, but significant software processing needed

## Slide 18
Quantum Good Privacy at Morgan State University
QGP Authentication Protocol Diagram. M: Message, H: Hash Functions (SHA 2/3), Hm: Hashed
message, Dis/Div: Dilithius Sign/Verify (PQC), ZIP/unZIP: Compression/Decompression, Es/Ds: Symmetric Key Encryption/Decroption, KYe/KYd: KYBER Encryption/Decryption (PQC)

## Slide 19
Quantum Courses Progression
QM for CS
Intro to QIS
Intro to QC
Applied QC
Quantum Algos
Quantum Crypto
Quantum Sensing
Quantum ML
Core 1-year Requirement
Quantum Computing Pipeline
FPGA Intro
Applied FPGA
Applied Quantum Pipeline
QM Lab 2
QKD Lab
Q-Sensing Lab
FPGA Lab I
FPGA Lab II
QM Lab 1

## Slide 20
Extras